Architect’s Specifications

Wireless discussion unit for use as delegate or chairman unit. Main delegate functions are to speak when the microphone is active or to listen to a speaker via the built-in loudspeaker or via connected headphones. Microphone activity is chairman controlled or manually controlled by the delegate when the microphone control button is pressed. Depending on system settings, the delegate is put on the request-to-speak list when the maximum of active microphones is reached, or directly when in chairman mode. Up to 150 delegate units can be used in one system in manual mode.

In addition the system operates fully automatically with intelligent voice detection. To avoid loss of the first consonants each delegate unit has a 50ms prerecording buffer, which will playback as soon as the voice detection system activates the microphone. To minimize an audible latency for the speaker, the system detects a 50ms pause during the speech to bring the played back audio in sync with the live audio signal with zero latency. Up to 50 units can be used in automatic mode.

Up to five open audio channels are used for the delegates, from which up to four can be reserved for chairmen.

Up to four audio return channels can be used for multilingual conference setups. The return channel can be selected at the delegate unit individually.

The main chairman can always mute all delegates by pushing and holding his talk button for more than two seconds. For easy installation there is no difference between chairman and delegate units. Every unit can be set to be chairman.

The system operates on Infrared technology for easy setup, no interference from other RF devices such as 2.4 GHz or 5.3 GHz WLAN or UHF wireless devices. Due to the principle of Infrared the system offers a secure audio transmission.

The built in loudspeakers and headphone jacks have a volume control. The loudspeaker stays on during speech so as not to confuse the user with a muted speaker. The system is designed to not produce acoustic feedback during speech.

The system offers two lengths of removable microphones with an illuminated ring for speech indication (on) or indication of cue position (blinking).

The delegate units can be operated on removable Li-ion battery packs or external power supplies.

The system offers control software with the following functions:

- Graphical setup of conference

- Name plates for each delegate unit

- Chairman priority mode via graphical user interface.

- Setting of gain and threshold settings for each delegate unit

- Video follows audio control

- Audio and Video recording

- Meta data recording which is synced to the audio and video recording

- Minute taking function

The system is open to be used with AMX/Crestron or similar control protocols.

Manufacturer: Audio-Technica

System: ATCS-60